## Slide 1
Nozzle throat mechanical cross sectional area is “actuatable” by multiplication factor after constraint period.
The area multiplication factor is changed from 1.0 to 0.9 gradually in this example.

## Slide 2
Input:
nozzle pressure ratio is increased

## Slide 3
Output:
mass flow rate via nozzle.
It decreases as throat area multiplication factor drops.

## Slide 4
Output:
throat mechanical cross sectional area.
It decreases as throat area multiplication factor drops.
Output:
“des” marked throat mechanical cross sectional area.
It is kept constant while throat area multiplication factor is changed.

## Slide 5
Components for design point constraint of mass flow rate is integrated into single component for easier handling.

## Slide 6
Mass flow rate signal is constrained to the value input as signal.
Constraint is kept until the time which is defined by “environment” block.
This component defines the time when mass flow rate constraint is removed and mechanical cross sectional area of nozzle throat turns from output to input.
Mechanical cross sectional area of throat is calculated variable when mass flow rate is constrained. “des” marked discrete variable stores that value.
After Mass flow rate constraint is removed, the value of mechanical cross sectional area is input and mass flow is calculated variable.
Change upstream pressure of nozzle after remove of mass flow rate constraint in order to check constraint become invalid and area is fixed.

## Slide 7
Input:
nozzle pressure ratio is increased

## Slide 8
Output:
mass flow rate through nozzle.
It is increased as nozzle pressure ratio rises.
Output:
signal into constraint block which constrains mass flow rate.
The value is fixed to 2 throughout the simulation, but does not affect on mass flow rate after constraint period.

## Slide 9
Output:
mechanical cross sectional area of nozzle throat.
It is calculated as output in period of mass flow constraint, and referred as input after constraint period.
Therefore, the value does not change when nozzle pressure ratio is increased.