## Slide 1
Ram pressurization.
Free stream velocity by flight gives compression to engine air.
Heat addition.
Heat (enthalpy) is given to flow. Essentially same as combustion chamber of other turbo-engines.
Ducts.
There are only ducts before & after combustion chamber. They behave as flow resistance (pressure drop component)
Principle of thrust generation is exactly same as that of turbojet.

## Slide 2
Heat addition.
-. Under constant volume
-. Intermittent combustion is necessary.
Single direction flow valve.
-. Make gas stream intermittent for intermittent.
-. Prevent gas from flowing backward under combustion period.
Flight velocity gives gas flow into engine.
This engine cannot start with zero-velocity.
Pipe (flow resistance) with volume effect.
-. Delay in mass flow.
No compression process in this thermodynamic cycle.

## Slide 3
Input:
-. Flight Mach number, or mach number of free-stream outside of engine.
-. It must be greater than zero value at the beginning. The start device provides inlet air with velocity in the real world.

## Slide 4
Input:
-. Temperature of combustion chamber.
-. Triangle wave in time domain simulating intermittent combustion.

## Slide 5
Input:
-. Temperature of combustion chamber. (Enlarged fig.)

## Slide 6
Output:
Net thrust of engine.(green)
Output:
-. Gross thrust of exhaust nozzle.(red)
-. Engine continues running after flight speed (inlet airspeed) gets zero.
Output:
Ram drag.(blue)

## Slide 7
Output:
Net thrust of engine.(green)
Output:
Gross thrust of exhaust nozzle.(red)
Output:
Ram drag.(blue)

## Slide 8
Output:
-. mass flow rate through engine.
-. Intermittent flow due to valve open/close.

## Slide 9
Output:
-. Pressure of combustion chamber.
-. Intermittent change.

## Slide 10
Adiabatic Compression
Const. Vol.
Heat Addition
Const. Vol.
Heat Rejection
Adiabatic Expansion
W
W
Q
Q
h
s

## Slide 12
MN
AoA
Alt
dm
Pt
Tt

## Slide 13
Fn

## Slide 14
AoA
MN
Alt
dm
Pt
Tt
dm
Pt
Tt

## Slide 15
pStd
Tstd
g

## Slide 23
Increase pressure ratio of compressor gradually.
Set drive power the “as calculated” variable.
Compress outside air.
Release heat to outside air.
absorb heat from room air.
Expand cycle air to outside pressure. The work generated by expansion is used for driving compressor.
heat
heat

## Slide 26
Fluid inlet port, input&output (use “connect” operator)
Fluid outlet port, input&output (use “connect” operator)
Expandable connector prepared for communication with internal variables which cannot be accessed by other ports,
input&output (use “connect” operator)
Flange (rotational mechanics port),
input&output (use “connect” operator)
Flange (rotational mechanics port),
input&output (use “connect” operator)
Pressure ratio;
input (use “connect” operator),
valid only when switchDetermine_PR==viaRealInput
Efficiency;
input (use “connect” operator),
valid only when switchDetermine_eff==viaRealInput

## Slide 31
Fluid inlet port, input&output (use “connect” operator)
Fluid outlet port, input&output (use “connect” operator)
Expandable connector prepared for communication with internal variables which cannot be accessed by other ports,
input&output (use “connect” operator)
Flange (rotational mechanics port),
input&output (use “connect” operator)
Flange (rotational mechanics port),
input&output (use “connect” operator)
Pressure ratio;
input (use “connect” operator),
valid only when switchDetermine_PR==viaRealInput
Efficiency;
input (use “connect” operator),
valid only when switchDetermine_eff==viaRealInput

## Slide 36
Fluid inlet port, input&output (use “connect” operator)
Fluid outlet port, input&output (use “connect” operator)
Fuel inlet port, input&output (use “connect” operator)
Lower Heating Value of Fuel;
input (use “connect” operator),
valid only when use_u_LHV_fuel==true
Efficiency of combustion;
input (use “connect” operator),
valid only when use_u_effComb==true
Fuel flow, output

## Slide 38
Mass flow rate signal is constrained to the value input as signal.
Constraint is kept until the time which is defined by “environment” block.
This component defines the time when mass flow rate constraint is removed and mechanical cross sectional area of nozzle throat turns from output to input.
Mechanical cross sectional area of throat is calculated variable when mass flow rate is constrained. “des” marked discrete variable stores that value.
After Mass flow rate constraint is removed, the value of mechanical cross sectional area is input and mass flow is calculated variable.
Change upstream pressure of nozzle after remove of mass flow rate constraint in order to check constraint become invalid and area is fixed.

## Slide 39
Input:
nozzle pressure ratio is increased

## Slide 40
Output:
mass flow rate through nozzle.
It is increased as nozzle pressure ratio rises.
Output:
signal into constraint block which constrains mass flow rate.
The value is fixed to 2 throughout the simulation, but does not affect on mass flow rate after constraint period.

## Slide 41
Output:
mechanical cross sectional area of nozzle throat.
It is calculated as output in period of mass flow constraint, and referred as input after constraint period.
Therefore, the value does not change when nozzle pressure ratio is increased.

## Slide 42
Components for design point constraint of mass flow rate is integrated into single component for easier handling.

## Slide 43
Nozzle throat mechanical cross sectional area is “actuatable” by multiplication factor after constraint period.
The area multiplication factor is changed from 1.0 to 0.9 gradually in this example.

## Slide 44
Input:
nozzle pressure ratio is increased

## Slide 45
Output:
mass flow rate via nozzle.
It decreases as throat area multiplication factor drops.

## Slide 46
Output:
throat mechanical cross sectional area.
It decreases as throat area multiplication factor drops.
Output:
“des” marked throat mechanical cross sectional area.
It is kept constant while throat area multiplication factor is changed.

## Slide 47
Mass flow rate which engine takes in at design point is constrained (= sizing of fluid components).
Constraint is kept until the time which is defined by “environment” block.
Rotational speed of engine shaft at design point is constrained (= sizing of rotary machines).
Constraint is kept until the time which is defined by “environment” block.
Mechanical cross sectional area of throat is calculated variable when mass flow rate is constrained. “des” marked discrete variable stores that value.
After Mass flow rate constraint is removed, the value of mechanical cross sectional area is input and mass flow is calculated variable.
This component defines the time when simulation switches from design-point to off-design.

## Slide 48
Input:
Combustor outlet temperature is constrained as input of engine rating.
It is increased in off-design simulation period.

## Slide 49
Output:
Mechanical rotational speed.
It is calculated as a result of input of combustor outlet temperature in off-design simulation period.
Output:
“des” marked mechanical rotational speed.
It is kept constant throughout simulation. Its value is defined in design-point calculation period.

## Slide 50
Output:
Mass flow rate which engine takes in.
It is calculated as a result of input of combustor outlet temperature in off-design simulation period.
Output:
“des” marked mass flow rate.
It is kept constant throughout simulation. Its value is defined in design-point calculation period.

## Slide 51
Actuate nozzle throat area size.
The area multiplication factor is changed from 1.0 to 0.9 gradually in this example.

## Slide 52
Input:
Combustor outlet temperature is constrained as input of engine rating.
It is increased in off-design simulation period. (10 [s] – 20 [s])
Input:
Multiplication factor of nozzle throat area.
It is decreased (closed) in off-design simulation period. (30 [s] – 40 [s])

## Slide 53
Output:
Mechanical rotational speed of engine shaft.
It is decreased as nozzle throat closes in order to compensate for the decrease in mass flow rate capacity.
Output:
Mass flow rate through nozzle.
It is decreased as nozzle throat area closes.

## Slide 54
Output:
Mass flow rate of fuel.
It is decreased as nozzle throat closes because the mass flow of air through engine is decreased but combustor outlet temperature is kept.
Output:
Gross thrust of nozzle.
It is decreased as mass flow capacity of nozzle and engine speed decreases.

## Slide 55
Add heat into hot volume. Constant volume heat addition & constant temperature expansion.
Reject heat from cold volume. Constant volume heat rejection & constant temperature compression.
Operating fluid moves between hot and cold volume.
Crank shaft.
90-deg phase difference between 2 rods.
Mechanical loss.
Connecting rods.
pistons.
Define positions of cylinders.
Fly wheel.

## Slide 56
Connecting rods.
pistons.
Crank shaft.
90-deg phase difference between 2 rods.
Animation window

## Slide 57
Input:
Temperature of hot heat source.

## Slide 58
Output:
gas temperature in hot cylinder.
Output:
gas temperature in cold cylinder.

## Slide 59
Output:
gas mass in hot cylinder.
Output:
gas mass in cold cylinder.

## Slide 60
Output:
rotational speed of crank-shaft.
It accelerates as hot heat source temperature is increased. However, it oscillates.

## Slide 61
Output:
Power via crank shaft.

## Slide 63
Output:
Heat flow from hot heat source into hot volume.
Output:
Heat flow out of cold volume.